## Slide 1
Lean Assessment System

## Slide 2: Introduction to Lean Overview
Agenda
What is the Lean Assessment?
Why Assess?
How the results are used
How the Assessment is conducted
Problems with the Assessment process
Areas of Assessment
Departments to be Assessed
Discussion – The Lean Vision

## Slide 3: What is the Lean Assessment?
An attempt to objectively quantify a subjective subject.
Investigates how well a department / facility / enterprise executes 10 Lean concepts and 40 Lean subjects.
Detailed questionnaire filled out by the operating management and an outside auditor.
  Specific scoring guidelines to help establish objectivity and consistency.

## Slide 4: What is the Lean Assessment?
WDGLL?
  What Does Good Look Like?
The assessment compares the facility to an ideal Lean operation.
It is very difficult to get a perfect score, since most factories are not completely Lean. A typical score for a good factory is around 40 points.

## Slide 5: What is the Lean Assessment?
Individual department scores are “rolled-up” to a facility score, and eventually to the entire enterprise.
Results are presented in a Visual Metric style.

## Slide 6: What is the Lean Assessment?
10 Lean Concepts
  5S
  Visual Metrics
  Standard Work
  Work Flow
  Quick Changeover
  Inventory Control & Production Scheduling
  Process Capability
  Total Productive Maintenance
  Associate Involvement
  Continual Improvement

## Slide 7: What is the Lean Assessment?
3 – 5 Subjects in each area

## Slide 8: What is the Lean Assessment?
Detail scoring guidelines for each subject
  Objective criteria specify how to score the subject

## Slide 9: What is the Lean Assessment?
1 – 5 points awarded for each subject area
Adds up to a total score for each Lean concept

## Slide 10: What is the Lean Assessment?
Trend chart of total score shows improvement over time.

## Slide 11: What is the Lean Assessment?
Radar chart of YTD total score shows strengths and weaknesses

## Slide 12: What is the Lean Assessment?
Detail numerical score data

## Slide 13: What is the Lean Assessment?
Improvement plan documentation
  This section is optional.
  You may use your existing project tracking systems.

## Slide 14: Why Assess Lean Performance?
“Whatever you measure gets better.”
Teaches Lean concepts to operating managers.
Drives improvements in a gentle, positive way.
  Makes incremental improvements easy to identify and plan.
  Provides self-imposed competitive pressure to improve.
Publicizes the need for Lean activities and helps build a Lean culture.

## Slide 15: How the Results are Used
Gathered for each manufacturing site.
Posted in a public location, inviting questions and comments from all associates.
Discussed in communication meetings.
Like all Lean communication, the emphasis will be on positive news:
  Who improved the most.
  Praise for the (expected) continual improvement.

## Slide 16: How the Assessment is Conducted
Break a facility into its “natural” pieces (usually its departments).
Form a Team to conduct the assessment
  Local Management
  Local Lean Champion
  Outside auditor
The Team tours the department and reviews:
  5S
  Metrics
  Process Flow Controls
  etc.
Team reads through the scoring guidelines and assigns scores based on the current, observed conditions.

## Slide 17: How the Assessment is Conducted
Repeat Step #2 & #3 until all the departments have been surveyed.
Departments are summed and averaged to create a total facility score.
Improvement plans (if any) may be documented at this point.
Results are publicly posted in the facility and discussed with operating associates.
  Good & Bad highlights mentioned
Repeat steps #1 – 6 for all facilities & create an enterprise composite score.

## Slide 18: Problems with the Assessment System
Like any measurement system, it has error.
Fundamentally, this is a subjective evaluation being forced into an objective framework. Bias is difficult to limit.
The results can be perceived as a negative if not handled properly
  Most facilities will receive a “low” score, since we are comparing to an ideal.
  All Lean concepts don’t always make sense in every situation.
  Equipment and business limitations often prevent adoption of good Lean practices.

## Slide 19: Problems with the Assessment System
How to Overcome the Problems:
Scores are reported as raw numbers without reference to the maximum.
  Improvement in the score is what is important and encouraged.
  Nobody gets fired for low scores; we praise those who improve or get high scores.
Outside auditor helps establish consistency between facilities.
Please remember: This is data, not a criticism.

## Slide 20: Areas of Assessment
5S
Visual Metrics
Standard Work
Work Flow
Quick Changeover
Inventory Control & Visual Scheduling
Process Capability
Total Productive Maintenance
Associate Involvement
Continual Improvement

## Slide 21: Areas of Assessment – 5S
The foundation for Lean... and all systematic improvements
Sort
    Only those things needed in the workplace are in the workplace. All other items are not present.
Set In Order
    “A place for everything, and everything in its place.”
Shine
    Formal shine schedules are used, and checked.
Standardize
    Labeling ensures the Set In Order is maintained, and standard work is encouraged.
Sustain
    Formal inspections and ratings of 5S are commonplace.

## Slide 22: Areas of Assessment – Visual Metrics
Instantly allow anyone to understand how well the operation is running, and where the challenges are.
Visual Display
    Measures of Safety, Quality, Delivery, and Cost are prominently displayed.
Update Method
    The person doing the work updates the data, using nothing more complex than a clipboard, stopwatch, and calculator.
Timeliness
    Metrics are current up to the most recent hour (or less).
Goal Oriented
    There is a goal for each metric which reflects the manager’s personal expectation.
Management Response
    Managers publicly respond to the metrics.

## Slide 23: Areas of Assessment – Standard Work
The ultimate goal of 5S, and the basis for all systematic improvement.
Work instructions
    Formal Work Instructions displayed at the work place.
Audited and Approved
    Work Instructions are ISO-style documents with formal approval, auditing, and revision procedures.
Training
    Associates are formally trained and tested, with a posted skills matrix.
Cross-Training
    Every associate can do every job.

## Slide 24: Areas of Assessment – Work Flow
The continuous and automatic flow of materials is desired.
Small Lot Sizes
    We should regularly manufacture in the smallest lot size purchased by the ultimate customer.
Pull System
    Physical signals initiate production of an item. Un-signaled products cannot be manufactured because there is no physical space for them.
Linked Operations
    Individual processes in a value stream are physically linked, ensuring synchronized FIFO flow.
Flexible Capacity
    Production capacity can be increased or decreased easily with minimal impact on costs.

## Slide 25: Areas of Assessment – SMED
Machine setup times are short, tracked, and produce good parts immediately.
Changeover Times
    Changeover time should be less than 5 minutes. (Last good piece to first good piece.)
Tracked Changeover Time
    All changeovers are publicly tracked with a visual metric, with goals, trends, and action items to improve.
Changeover Work instructions
    Formal ISO-style Work Instructions exist which detail the changeover procedure.
Presets
    Equipment are set to hard stops and presets so that they make good products immediately.

## Slide 26: Areas of Assessment – Inv Ctrl/Sched
Simple scheduling and inventory control systems exist. Every associate knows what product must be run next.
Kan Bans
    Kan Bans are used for supplies and raw materials, and some Finished Goods.
Visual Schedules
    Schedules are prominently displayed. Schedule attainment is immediately obvious.
Update Period
    The schedule should be updated very frequently (hourly if possible).
Sequencing Authority
    Associates should have the authority to alter the sequence for efficiency within very specific guidelines, which include knowledge of our commitments to the customer.

## Slide 27: Areas of Assessment – Capability
Statistical tools are used to demonstrate process capability. Pokes Yokes are used for mistake proofing.
SPC
    Statistical Process Control is used on critical characteristics. Control limits are regularly updated. Out of Control Work Instructions exist.
6-Sigma
    Most of the technical and managerial staff are LSS Black Belts, and have active projects underway.
Gages
    ISO-style gage control is in place, and most gages have a P/T ratio < 0.1.
Poke Yokes
    New Poke Yoke devices are being continually added as new failure mechanisms occur.

## Slide 28: Areas of Assessment – TPM
Equipment maintenance from a Lean perspective.
Overall Equipment Effectiveness (OEE)
    OEE is recalculated weekly for most equipment. Significant improvements in OEE have been achieved over the past year.
Traditional Preventative Maintenance
    A solid traditional PM is in place.
Visual Daily PM (Autonomous Maintenance)
    Operators do daily PM checks which are publicly identified and recorded.
Visual Logs
    The PM status of each machine can be immediately determined by glancing at a prominently displayed metric board.

## Slide 29: Areas of Assessment – Involvement
We want a “Lean Culture”. Associates are continually and actively working on Lean improvements, with minimal managerial oversight.
LSS Training
    Extensive formal training has been given to all associates.
Kaizen Blitz Events
    Blitz events occur regularly, and have included a very large majority of the associates.
Improvement Projects
    Most associate have completed a Lean project within the last year. These projects are documented and posted on communication boards. Gifts of nominal valued are given to some participants.

## Slide 30: Areas of Assessment – Improvement
Lean enterprises continually improve in Labor, Quality, and Inventory. This is a catch-all for any improvements not driven by capital investment.
Labor Improvements
    Significant improvements in Labor effectiveness should have been achieved over the past year.
Quality Improvement
    Significant improvements in quality should have been achieved over the past year.
Inventory Improvements
    Significant reductions in total inventory (measured in “days”) should have been achieved over the past year.

## Slide 31: Departments to be Assessed
  Discussion: What departments to assess?

## Slide 32: The End
Any Questions

## Slide 33: The End
Thank You!

## Slide 34: Discussion The Lean Vision